# SEP #53 : Extend “fullpath” to manage matrix of string as input argument

Title: extends fullpath
Version: 1.0
Author: Allan CORNET (allan.cornet@scilab.org)
Review:
Commented:
State:
Scilab-Version: 5.4
Vote:
Created: 17th December 2010

### Abstract

Extend 'fullpath' to manage matrix of strings (filenames)
This function generates a full path to a file or directory.

### Rationale

Current 'fullpath' works only with a string as input argument.
Use a matrix of string will be easier and faster than to do a scilab loop on 'fullpath'

### Example Usage

cd(TMPDIR);
mkdir(TMPDIR + "/niv1");
mkdir(TMPDIR + "/niv1/niv2");
mkdir(TMPDIR + "/niv1/niv2/niv3");
mputl(' ', TMPDIR + "/niv1/test1.txt");
mputl(' ' , TMPDIR + "/niv1/niv2/test2.txt");
cd(TMPDIR + "/niv1/niv2/niv3");

M = ["../../test1.txt", "../test2.txt"];

// Scilab 5.3 and previous version:

for i=1:size(M, "*")
  disp(fullpath(M(i));
end

// Scilab 5.4:
R = fullpath(M);
disp(R);

### Changelog
1.0 – Initial Revision
### Copyright
This document has been placed under the license CeCILL-B.