SEP #114: New function bicg (BiConjugate Gradient method).

Version: 1.0
Author: Paul Bignier
Review:
Commented:
State:
Scilab-Version: 5.4.0
Created: Oct 23 2013

Abstract
The aim of this SEP is to present the new function bicg, which implements the BiConjugate Gradient method to solve linear systems.

Rationale
To solve A*x=b linear systems, Scilab proposes the pcg function (Preconditioned Conjugate Gradient method), which requires A be symmetric positive definite.
bicg only needs A be square.

The inputs and outputs of bicg are the same as pcg.

Calling Sequence
The available calling sequence is:

   [x, [flag, [err, [iter, [res]]]]] = bicg (A, b [, tol [, maxIter [, M [, M2 [, x0 [, verbose]]]]]])
   [x, [flag, [err, [iter, [res]]]]] = bicg (A, b [key=value,...])

Example Usage

// Seven input arguments and all output arguments
A = [10 1; 1 10];
b = [11; 11];
tol = 100*%eps;
maxit = 10;
M1 = [1 0; 0 1];
M2 = [1 0; 0 1];
x0 = [1; 1];
[xcomputed, flag, err, iter, res] = bicg(A, b, tol, maxit, M1, M2, x0)
// xexpected = [1; 1]

// Special case where b = 0
A = [100 1; 1 10];
b = [0; 0];
[xcomputed, flag, err, iter, res] = bicg(A, b)
// xexpected = [0; 0];

Changelog
– Initial Revision
Copyright
This document has been placed under the license CeCILL-B - © Scilab Enterprises