SEP #113: New function conjgrad as gateway to the Conjugate Gradient family solvers. pcg obsolete as it is.

Version: 1.0
Author: Paul Bignier
Review:
Commented:
State:
Scilab-Version: 5.4.0
Created: Oct 24 2013

Abstract
The aim of this SEP is to present the new function conjgrad, which is a gateway to chose from:
- “pcg” (Predonditioned Conjugate Gradient),
- “cgs” (predonditioned Conjugate Gradient Squared),
- “bicg” (predonditioned BiConjugate Gradient) and
- “bicgstab” (predonditioned BiConjugate Gradient Stabilized) linear system solvers.

Rationale
To solve A*x=b linear systems, Scilab proposes the pcg function (Preconditioned Conjugate Gradient method).
conjgrad introduces three new solvers: “cgs”, “bicg” and “bicgstab” selectable from an input argument.

As it is, the pcg function will be obsolete and calling pcg(A, b,...) shall be replaced by conjgrad(A, b, “pcg”,...).

By default, conjgrad selects “bicgstab”.

The inputs and outputs of conjgrad are the same as Matlab’s pcg, cgs, bicg and bicgstab commands.

Calling Sequence
The available calling sequence is:

[x, [flag, [err, [iter, [res]]]]] = conjgrad (A, b [, method [, tol [, maxIter [, M [, M2 [, x0 [, verbose]]]]]]])
[x, [flag, [err, [iter, [res]]]]] = conjgrad (A, b [, method [, key=value,...]])

Example Usage

// Seven input arguments and all output arguments
A = [10 1; 1 10];
b = [11; 11];
tol = 100*%eps;
maxit = 10;
M1 = [1 0; 0 1];
M2 = [1 0; 0 1];
x0 = [1; 1];
[xcomputed, flag, err, iter, res] = conjgrad(A, b, “pcg”, tol, maxit, M1, M2,x0)
[xcomputed, flag, err, iter, res] = conjgrad(A, b, “cgs”, tol, maxit, M1, M2,x0)
[xcomputed, flag, err, iter, res] = conjgrad(A, b, “bicg”, tol, maxit, M1,M2,x0)
[xcomputed, flag, err, iter, res] = conjgrad(A, b,“bicgstab”,tol,maxit,M1,M2,x0)

// xexpected = [1; 1]

// Special case where b = 0
A = [100 1; 1 10];
b = [0; 0];
[xcomputed, flag, err, iter, res] = conjgrad(A, b) // Selects bicgstab
[xcomputed, flag, err, iter, res] = conjgrad(A, b, ”pcg”)
[xcomputed, flag, err, iter, res] = conjgrad(A, b, ”cgs”)
[xcomputed, flag, err, iter, res] = conjgrad(A, b, ”bicg”)
[xcomputed, flag, err, iter, res] = conjgrad(A, b, ”bicgstab”)
// xexpected = [0; 0];

Changelog
– Initial Revision
Copyright
This document has been placed under the license CeCILL-B - © Scilab Enterprises